7W Shine Disk Light Energy Saving Lamp

KCF07DSK/GX53-830     KCF07DSK/GX53-865

Product Code Format:

KCFDSK/-

Features:

- Save energy up to 80% comparing with incandescent lamps

- Long Life of 8000h, 8 times longer than incandescent lamp

- Amalgam technology to achieve premium performance and minimum Hg content (2mg)

- High efficient tri-phosphor coating with excellent color rendering.

- Not dimmable

- Lamp life may reduce when used in a enclosed fitting

Specifications:

| Rated Lamp Wattage | 7W | Ambient Temperature- | 0oC to 40oC |
| --- | --- | --- | --- |
| Equ. Watt | 35W | Lux @ 1.0m | 76lx |
| Voltage | 220-240V | Lux @ 2.0m | 19lx |
| Line Frequency | 50/60Hz | Start Time | 0.6s |
| Input Current | 50mA | Warm up Time (60%) | 40s(Norm.), 60s(Max) |
| Dimmable | No | Switch Cycles | 10,000 Times |
| Base | GX53 | Length | 29mm |
| Energy Class | A | Diameter | 74mm |
| Life to 50% failure | 8000hr | Packaging type | Colour Box |
| Colour Temperature | 3000K/6500K | Qty per Box | 1 |
| Mercury (Hg) | 2mg | Qty per mid-Carton | 10 |
| CRI | 82 | Qty per Carton | 50 |
| Lamp Luminous Flux | 350lm | Net weight Per piece | kg |
| Lumen maintenance 2000h | 85% | Gross Weight per Carton | 6.02kg |
| Lumen maintenance 8000h | 70% |  |  |

# Text boxes

Rated Lamp Wattage

Colour Temperature

Lamp Cap