Applications
Dimmable	Yes
Burning position	any

Categorizations
ILCOS	HRGS//UB-50-12-GU5,3-51/36

General Description
Base (standard designation)	GU5.3
Mercury-free	Yes

Technical – Electrical Data
Nominal wattage (packaging)	50 W
Construction wattage	50 W
Nominal voltage	12 V

Technical – Geometries
Overall length	45.00 mm
Contact spacing	5.3 mm
Diameter	51.0 mm
Length	46.00 mm

Technical – Light Technical Data
Luminous intensity	1150 cd
Beam angle	36 °
Color temperature	2950 K
Color rendering index Ra	100
Rated starting time	0 s

Packaging units / Product code Packaging unit Pieces/ Unit Dimensions in h x w x l Gross weight Volume / 4050300857701 Folding carton box (contains 1 Piece) 0,000 mm x 0,000 mm x 0,000 mm 0,000 g (36,000 g) 0,000 Cubic dec. / 4050300857718 Shipping carton box (contains 20 Piece) 123,000 mm x 105,000 mm x 238,000 mm 0,786 kg (0,720 kg) 3,074 Cubic dec.

Every professional knows that light is not always the same when it comes to illuminating heatsensitive objects. In this case the DECOSTAR 51 dichroic reflector lamp is the right choice because most of the heat produced by the lamp is emitted through the rear of the reflector. This reduces the heat in the light beam by up to 66 %. It is therefore easier to present heat-sensitive objects in the right light. / Brilliant accent light / Dichroic reflector reduces the heat in the light beam by up to 66 % / Approved for use in open luminaires to IEC 60598-1 / Average life: 2,000 h / Dimmable / Ra=100 / Color temperature: 20 W – 2,800 K; 35 W – 2,900 K; 50 W – 2,950 K / Base: GU5.3 / UV filter / For light distribution curves go to www.osram.com